## Slide 1: Lab 6: Conditional Branching and Control Flow in MIPS

## Slide 2: Learning Objectives
Explain how branch instructions control program flow in MIPS.
Use beq and bne to implement conditional decisions.
Use slt and slti to compare values.
Translate C-style if and if–else statements into MIPS.
Implement while loops using branch and jump instructions.
Trace program execution using QtSPIM.

## Slide 3: Common Arithmetic and Comparison Instructions
Instruction | Meaning
add rd, rs, rt | Add two registers
sub rd, rs, rt | Subtract two registers
mul rd, rs, rt | Multiply register values
sll rd, rt, shamt | Shift left
srl rd, rt, shamt | Shift right logical
sra rd, rt, shamt | Shift right arithmetic
slt rd, rs, rt | Set rd = 1 if rs < rt; otherwise 0
slti rt, rs, imm | Set rt = 1 if rs < immediate; otherwise 0
Remember: slt and slti produce a value of either 0 or 1.

## Slide 4: Memory Access and System Calls
Instruction | Meaning
lw rt, label | Load a word from memory
sw rt, label | Store a word in memory
Memory Access Instructions
Common QtSPIM System Calls
$v0 | Service
1 | Print integer
4 | Print string
10 | Exit program
Example: Print an Integer
  move $a0, $s2
  li $v0, 1
  syscall

## Slide 5: Common Branch Instructions
Instruction | Meaning | Condition
beq rs, rt, label | Branch if equal | rs == rt
bne rs, rt, label | Branch if not equal | rs != rt
Example 1: Branch if Equal
  li $t0, 5
  li $t1, 5
  beq $t0, $t1, L1
  addi $s0, $s0, 1 # Skipped
  L1:
  # Branch target
Example 2: Branch if Not Equal
  li $t0, 5
  li $t1, 7
  bne $t0, $t1, L1
  addi $s0, $s0, 1 # Skipped
  L1:
  # Branch target
beq and bne compare registers for equality or inequality. For conditions such as less than, we can use slt.

## Slide 6: Common MIPS Registers
Register | Typical Use
$t0–$t9 | Temporary values
$s0–$s7 | Saved registers
$zero | Constant value 0
$a0–$a3 | Function arguments
$v0 | Return value or syscall service
Example:
  li $s0, 5
  li $s1, 3
  slt $t0, $s0, $s1
Since 5 < 3 is false:
  $t0 = 0
If the comparison were true, $t0 would contain 1.

## Slide 7: Conditional Operations in MIPS
Programs use conditional operations to make decisions and repeat instructions.
C-style If–Else
  if (a == b)
  x = x + 1;
  else
  x = x - 1;
C-style While Loop
  while (i < 5)
  i++;
MIPS Control-Flow Instructions
Instruction | Purpose
beq | Branch when two registers are equal
bne | Branch when two registers are different
slt | Test whether one register is less than another
j | Jump unconditionally
Important: A label identifies a location in the program that a branch or jump can target.

## Slide 8: Example 1: If–Else If–Else
Translate the following C-style program into MIPS assembly.
  int a = 5;
  int b = 3;
  int result;
  if (a < b)
  {
  result = a + b;
  }
  else if (a == b)
  {
  result = a * b;
  }
  else
  {
  result = a - b;
  }
Register Mapping
a → $s0
b → $s1
result → $s2
Requirements: Use slt, beq or bne, labels, and j.
Expected Result: Since 5 < 3 is false and 5 == 3 is false, the final result is 5 − 3 = 2.

## Slide 9: MIPS Solution
.data
a: .word 5
b: .word 3
result: .word 0
newline: .asciiz "\n"
.text
.globl main
main:
# Load a and b
lw $s0, a
lw $s1, b
# if (a < b)
slt $t0, $s0, $s1
bne $t0, $zero, LESS
# else if (a == b)
beq $s0, $s1, EQUAL
# else: result = a - b
sub $s2, $s0, $s1
j STORE
LESS:
add $s2, $s0, $s1
j STORE
EQUAL:
mul $s2, $s0, $s1
STORE:
# Store result
sw $s2, result
# Print result
move $a0, $s2
li $v0, 1
syscall
# Print newline
la $a0, newline
li $v0, 4
syscall
# Exit
li $v0, 10
syscall
Output: 2

## Slide 10: Example 2: While Loop with If–Else
Translate the following C-style program into MIPS assembly.
  int i = 0;
  int sum = 0;
  while (i < 5)
  {
  if (i % 2 == 0)
  sum = sum + i;
  else
  sum = sum - i;
  i++;
  }
Program Logic
  If i is even, add i to sum.
  If i is odd, subtract i from sum.
  Continue while i < 5.
Register Mapping
i → $t0 sum → $t1
i = 0 → sum = 0
i = 1 → sum = -1
i = 2 → sum = 1
i = 3 → sum = -2
i = 4 → sum = 2
Result: 2

## Slide 11: MIPS Solution
.data
newline: .asciiz "\n"
.text
.globl main
main:
li $t0, 0 # i = 0
li $t1, 0 # sum = 0
li $t2, 5 # loop limit
LOOP:
# while (i < 5)
slt $t3, $t0, $t2
beq $t3, $zero, END
# Check whether i is even
andi $t4, $t0, 1
beq $t4, $zero, EVEN
ODD:
sub $t1, $t1, $t0
j CONTINUE
EVEN:
add $t1, $t1, $t0
CONTINUE:
addi $t0, $t0, 1
j LOOP
END:
# Print sum
move $a0, $t1
li $v0, 1
syscall
# Print newline
la $a0, newline
li $v0, 4
syscall
# Exit
li $v0, 10
syscall
Output
2

## Slide 12: In-Class Task 1: If–Else
Translate the following C-style program into MIPS assembly.
  int x = 8;
  int y = 5;
  int z;
  if (x < y)
  z = x + y;
  else
  z = x - y;
Register Mapping
  x → $s0 y → $s1 z → $s2
Requirements
  Load x and y.
  Compare the values using slt.
  Use a branch instruction to implement if–else.
  Store the final result in z.
  Print z in QtSPIM.
Expected Output
Since 8 < 5 is false, the else block executes:
z = 8 – 5 = 3

## Slide 13: In-Class Task 2: While Loop and If–Else
Translate the following C-style program into MIPS assembly.
  int i = 0;
  int sum = 0;
  while (i < 6)
  {
  if (i < 3)
  sum = sum + i;
  else
  sum = sum - i;
  i++;
  }
Register Mapping
  i → $t0 sum → $t1
Requirements
  Implement the while (i < 6) condition.
  Implement the if (i < 3) condition.
  Update sum correctly.
  Increment i after each iteration.
  Use slt, beq or bne, and labels.
  Print the final value of sum.
Expected Calculation
  i = 0 → sum = 0
  i = 1 → sum = 1
  i = 2 → sum = 3
  i = 3 → sum = 0
  i = 4 → sum = -4
  i = 5 → sum = -9
Result: −9

## Slide 14: Summary: Conditional Branching in MIPS
beq: Branches when two registers contain equal values.
bne: Branches when two registers contain different values.
slt: Sets a register to 1 if one value is less than another; otherwise 0.
slti: Compares a register against an immediate value.
j: Transfers control unconditionally to a label.
Labels: Identify locations that branches and jumps can target.
MIPS combines comparison instructions, conditional branches, unconditional jumps, and labels to
implement if, if–else, and while constructs.